DRAFT

April 2, 2018

AISI – OP Committee

850 OP Work Order – Specification

ASC X12 – Version 004010

ISA*00*          *00*          *01*444555666      *01*111222333         *180402*1114*U*00400*000000001*0*P*~

GS*PO*444555666*111222333*20180402*1114*01*X*004010

ST*850*0001

BEG*00*TC*TV19710-01**20180402*01

REF*PR*ABC123		(Price Quotation Number)

REF*C1*AB5557

REF*C3*55566688

PER*CR*STEEL PRODUCER SALES REP NAME*TE*555-123-4567*FX*513-123-9999

FOB*PP

DTM*007*20180402*0609

PID*S**ST*02***8		(Major Product)

PID*S**ST*08***35A       	(Coil Group)

PID*S**ST*34***22		(Mill Edge)

PID*S**ST*74***20B		(Winding/Surface Orientation)

PID*S**ST*135***13		(Quality Designation)

PID*S**ST*40*EXXON LIGHT BRAND**18B  (Surface Treatment –Oil)  NOTE:NOT APPLICABLE

TO PRODUCT

PID*F****GALVANIZED PRODUCT - COIL / FLAT - NOT PAINTED

PID*F****BARP:193156

PID*F****DEST:SINGLE BILLING BASIS C  STORAGE

PID*F****DEST:WECOAT METALS

PID*F****DEST:PORTAGE  US HIGHWAY 12 AT INDIANA

PID*F****DEST:RT249  PORTAGE, IN 46368

PID*F****FOB:MILL

PID*F****INSP:01 MILL INSPECTION RA/SN ALSO RA/LT REPORT , BASE METAL

THICKNESS,

PID*F****PROD:GALVANIZE CARBON

PID*F****REQ:SW0101

PID*F****SPEC:ASTM A653-05 GR 80 CLASS 1 MILL APPROVAL REQUIRED SS AS COATED

EXPOSED P

PID*F****SPEC:RIME SIDE OUT G40 MIN SPANGLE NO CHEM TREAT OIL MEDIUM   PICKLE

WELD OK-LIM

PID*F****SPEC:IT 1 YS MIN 80. KSI TS MIN 82. KSI LONGITUDINAL ASTM STD TENS

PID*F****STKX:STKX 13424               FROM                                       543

PID*F****TOL:GAUGE: A924 TABLE 3 +0.0040/- 0 1" FROM EDGE , WIDTH: USS STD

WIDTH TOL

PID*F****TOL:+.1875/-0., FLAT: ASTM STD FLAT TOL

PID*F****TRF:TL-B-40M-C-PPD

MEA*OD*TH*0.0276*ED

MEA*OD*TH*0.7*MB

MEA*OD*WD*54.3307*ED

MEA*OD*WD*1380*MB

MEA*SD*TH*0.0276*EM

MEA*SD*TH*0.70104*MZ

MEA*SD*WD*54.3307*ED

MEA*SD*WD*1379.99978*MB

MEA*SD*ID**IN*24

MEA*SD*ID**MM*609.6

MEA*SD*OD**IN**84

MEA*SD*OD**MM**2133.6

MEA*WT*WT*0*LB*52805*66006

MEA*WT*WT*0*KG*23952*29940

PWK*MD**FX*****FAX TEST REPORT TO STEEL PRODUCER, JOHN SMITH @ 615-111-4444

PKG*X*34*AS*2M10*COMMENTS		(Product Marking Code or Text Instructions)

PKG*X*36*AS*2P83P12*COMMENTS	(Product Packaging Code or Text Instructions)

PKG*X*ZZ*AS*2L86*COMMENTS   	(Load Code or Text Instructions) (ZZ Mutually agreed upon as Load #)

N1*MF*PROTEC*1*006985097

N1*SU*PROTEC*1*006985097

N1*OU*OP NAME*1*666555444

N1*SF*PRIOR OP*1*333222111

N1*BY*CUSTOMER NAME *1*333333333

N3*1001 BEST STREET

N4*BROWNSVILLE*TX*78520

N1*ST*SHIP TO NAME*91*3329660-008

N2*C/O RIO GRANDE FWD CO INC

N3*6333 EAST 14TH ST

N4*BROWNSVILLE*TX*78520

TD5*O*2*AAAA*M*AAAA TRUCKING*CL

PO1*01*50000*LB***VO*TV19710*VN*001*HN*T123456*GC*A630*VX*3.01E+08*

PO*241240588-B*BP*112*XX*20.3*KF*`1000*A6*STD

LIN**PD*PRODUCT DESCRIPTION*SF*SURFACE FINISH*TP*PRODUCT TYPE

CTP**CON*9.99*1000*LB****HP

MEA*PD*TH*0.0276*EM*0.0256*0.0296

MEA*PD*TH*0.70104*MZ*0.6502*0.7518

MEA*DT*TH**EM*0.002*0.002

MEA*DT*TH**MZ*0.0508*0.0508

MEA*PD*WD*54.3307*ED*54.3307*54.6063

MEA*PD*WD*1379.99978*MB*1379.9998*1387

MEA*DT*WD**ED**0.2756

MEA*DT*WD**MB**7.0002

MEA*PD*ID**IN*24

MEA*PD*ID**MM*609.6

MEA*PD*OD**IN**66.39

MEA*PD*OD**MM**1686.31

MEA*WT*WT*0*LB*15432*46297

MEA*WT*WT*0*KG*7000*21000

PID*S**ST*05***66A	(Slit)

PID*F****FREE FORM PROCESSING INSTRUCTIONS

PID*F****FREE FORM PROCESSING INSTRUCTIONS

PID*F****FREE FORM PROCESSING INSTRUCTIONS

PID*S**ST*08***35A       	(Coil Group)

PID*S**ST*34***22		(Mill Edge)

PID*S**ST*74***20B		(Winding/Surface Orientation)

PID*S**ST*05***8                  (Major Product)

PID*S**ST*40*EXXON LIGHT BRAND**18B  (Surface Treatment –Oil)  NOTE:NOT APPLICABLE

TO PRODUCT

REF*SE*AB5557

REF*RV*55566688

DTM*007*20180402*0909

SCH*57234*LB***077*20180602	(Process Week)

PO1*01*50000*LB***VO*TV19710*VN*001*HN*T123456*GC*A630*VX*3.01E+08*

PO*241240588-B*BP*112*XX*20.3*KF*`1000*A6*STD

LIN**PD*PRODUCT DESCRIPTION*SF*SURFACE FINISH*TP*PRODUCT TYPE

CTP**CON*9.99*1000*LB****HP

MEA*PD*TH*0.0276*EM*0.0256*0.0296

MEA*PD*TH*0.70104*MZ*0.6502*0.7518

MEA*DT*TH**EM*0.002*0.002

MEA*DT*TH**MZ*0.0508*0.0508

MEA*PD*WD*54.3307*ED*54.3307*54.6063

MEA*PD*WD*1379.99978*MB*1379.9998*1387

MEA*DT*WD**ED**0.2756

MEA*DT*WD**MB**7.0002

MEA*PD*ID**IN*24

MEA*PD*ID**MM*609.6

MEA*PD*OD**IN**66.39

MEA*PD*OD**MM**1686.31

MEA*WT*WT*0*LB*15432*46297

MEA*WT*WT*0*KG*7000*21000

PID*S**ST*14**NT*66A	(Edge Trim)

PID*F****FREE FORM PROCESSING INSTRUCTIONS

PID*F****FREE FORM PROCESSING INSTRUCTIONS

PID*F****FREE FORM PROCESSING INSTRUCTIONS

PID*S**ST*08***35A       	(Coil Group)

PID*S**ST*34***22		(Mill Edge)

PID*S**ST*74***20B		(Winding/Surface Orientation)

PID*S**ST*05***8                  (Major Product)

PID*S**ST*40*EXXON LIGHT BRAND**18B  (Surface Treatment –Oil)  NOTE:NOT APPLICABLE

TO PRODUCT

REF*SE*AB5557

REF*RV*55566688

DTM*007*20180402*0909

SCH*57234*LB***077*20180602 (Process Week)

CTT*2

SE*123*0001

GE*1*01

IEA*1*000000001

# Text boxes

Incoming Dimensions “As Received”

Master and Previous OP Material IDs

Preferred Carrier

Packaging Instructions

Product Description /Specifications

Master and Previous OP Material IDs

Shipping Instructions

Customer Ordered  Dimensions

Honda MSA # and Nomenclature

Exit Dimensions – First Process

Paperwork Instructions

Exit Dimensions – Second Process